## Slide 1: Static optimization and Introduction to variational calculus

## Slide 2: Static optimization
Minimize a function f(x) 𝞊 R, x 𝞊 Rn; x = {x1, … , xn}
Necessary conditions of optimality (unconstrained case)
  del (f(x))/del(x) = 0 ……. How many equations …..
    del (f(x))/del(x1) = 0
    del (f(x))/del(x2) = 0
    .
    .
    del (f(x))/del(xn) = 0
  [del (f(x))/del(x1); del (f(x))/del(x2); …; del (f(x))/del(xn)] = [0; 0; …., 0]
  f(x) = f(x1, x2, x3) = (x1 )2 +(x2 )2 +(x3 )2 Unique solution
  f(x) = f(x1, x2, x3) = (x1+x2 )2 +(x3 )2 Infinite solutions / multiple solutions
  f(x) = f(x1, x2, x3) = (x1 )2 +(x3 )2 Infinite solutions
  f(x) = f(x1, x2, x3) = cos(x1 ) + sin(x2) + (x3 )2 Infinite solutions
  (under the domain constraint of [0, pi/2] we could have got a unique solution.)
  (under the domain constraint of [0, pi/6] we could have got no solution.)

## Slide 3: Static optimization
Minimize a function f(x) 𝞊 R, x 𝞊 Rn; x = {x1, … , xn}
Under the constraints :
  Nonlinear constraint : g(x) (there could be m constraints)
    Equality constraints g(x) = 0
    Inequality constraint g(x) <= 0 (g(x) is less than or equal to)
Necessary conditions of optimality (constrained case, equality constraints)
  Augmented cost function : J = f + ƛT g ( dimension of ƛ 𝞊 Rmx1 ). (J is scalar)
  Number of free variables / independent variables in J : n + m
    Increased the dimensionality of the problem
  Del(J)/del(x) = 0 del(f)/del(x) + (del(g)/del(x)) ƛ = 0. ---- n eqns
  Del(J)/del(ƛ) = 0 g(x) = 0 ---- m eqns
f(x) = f(x1, x2, x3) = (x1+x2 )2 +(x3 )2
g(x) = x1 - x2 = 0
g(x) = sin(x1) + cos(x2) = 0
Unique solution
Multiple/ infinite solution

## Slide 4: Static optimization
Under the constraints
  Inequality constraint g(x) <= 0 (less than or equal to)
  Karush-Kuhn-Tucker condition is used to find the optimality
  The constraints can be divided in two types
    Active constraints => when the solution tries to cross the boundary, gi(x) = 0
    Inactive constraints => when the solution is well within the boundary (we just forget about the presence of constraint)
    We have to always solve the problem for the active constraints only. (without bothering about the inactive constraints)

## Slide 5: Basic concepts of variational calculus
Functional ( the argument is a function and output is a scalar value)
J(x(t)) = (t0 to tf) ∫ (x(t))2 dt : x(t) could be any admissible function
            : x(t) = 0. / x(t) = log(x). / x(t) = sin(t). / x(t) = e^t. / x(t) = t+0.1*t^2 / ………
    Min J(x(t)) => x(t) = 0
J(x+𝛿x) => 𝛿x: is a small change in the function x (however 𝛿x is a function in itself, it can have any admissible form)
Only major requirement is that value of : x+𝛿x = x(t)+𝛿x(t) should not be very far from the value of x(t) for all t 𝞊 [t0 , tf]
Increment
  ΔJ = J(x+𝛿x) - J(x)
  First order variation
    We consider the only first order terms in the increment

## Slide 6
t0
tf
x(t)
x(t)+𝛿x(t)
𝛿x(t)
0

## Slide 7: First order variation example
ΔJ = J(x+𝛿x) - J(x)
= ∫ (x+ 𝛿x)2 dt - ∫ (x)2 dt (integral limits t0 to tf are assumed to be there)
= ∫ [(x+ 𝛿x)2 - (x)2 ] dt
= ∫ [2 x(t) 𝛿x(t) + 𝛿x(t)2] dt
𝛿J(x, 𝛿x ) = First order variation
(considering the terms upto first order approximation only)
= 2 ∫ (x(t) 𝛿x(t)) dt = 0. any 𝛿x(t)=1, 2, sin(t), cos(pi/4*t)*0.001
X*(t) = 0
Fundamental theorem of calculus of variation
𝛿J(x*, 𝛿x ) = 0, for all admissible 𝛿x(t), then x*(t) is the extremal (minimum or maximum)

## Slide 8
ΔJ (x*, 𝛿x) = J(x*+𝛿x) - J(x*)
Assume that x* = sin(t) + t e^t + t^3/6. => this gives minimum value of J(x(t)) = int 0 to 1 int(x(t)+e^x(t)) dt
ΔJ >= 0 for all admissible 𝛿x, if x* is minimum then for 𝛿x->0
ΔJ (x*, 𝛿x) = 𝛿J(x*,𝛿x) +g(x*,𝛿x) |𝛿x|
𝛿J(x*,𝛿x) = 0 at the extremal for all admissible 𝛿x(t). (page 121 , Kirk)
Suppose the functional is
J(x) = (t0 to tf) ∫ g(t,x,x_dot)dt (very important from practical considerations)

## Slide 9: Euler Lagrange equation Fixed initial & final state and fixed initial & final time)
J(x) = (t0 to tf) ∫ g(t,x,x_dot)dt
ΔJ(x, 𝛿x) = J(x+𝛿x) - J(x)
= (t0 to tf) ∫ g(t,x+ 𝛿x,x_dot+ 𝛿x_dot)dt - (t0 to tf) ∫ g(t,x,x_dot)dt
= (t0 to tf) ∫ (g(t,x+ 𝛿x,x_dot+ 𝛿x_dot) - g(t,x,x_dot))dt
= (t0 to tf) ∫ (g(t,x+ 𝛿x,x_dot+ 𝛿x_dot) - g(t,x,x_dot))dt
Taylor series expansion upto first order terms
g(t,x+ 𝛿x,x_dot+ 𝛿x_dot) = g(t,x,x_dot) + del(g)/del(x) 𝛿x+ del(g)/del(x_dot) 𝛿x_dot+HOT

## Slide 10: Special case : Fixed initial & final state and fixed initial & final time
𝛿J(x, 𝛿x) = (t0 to tf) ∫{del(g)/del(x) 𝛿x+ del(g)/del(x_dot) 𝛿x_dot} dt
Using integration by parts
  ((t0 to tf) ∫f*g dt = [f ∫ g dt] (t0 to tf) - (t0 to tf) [∫((df/dt) ∫ g dt) dt] )
= [del(g)/del(x_dot) 𝛿x] (t0 to tf) + (t0 to tf) ∫{del(g)/del(x) - d/dt{del(g)/del(x_dot)} 𝛿x dt
Initial and final states are fixed
(x(t0) = x0, x(tf) = xf)
There will be no variation in initial and final
state => 𝛿x(t0) = 0 = 𝛿x(tf)
⍺(t0) = x0, ⍺(t0)+𝛿x(t0) = x0 => 𝛿x(t0)=0
xf
x0
t0
tf

## Slide 11: Special case : Fixed initial & final state and fixed initial & final time
𝛿J(x*, 𝛿x) = (t0 to tf) ∫[del(g)/del(x) - d/dt{del(g)/del(x_dot)}] 𝛿x(t) dt = 0
Euler equation
del(g)/del(x) - d/dt{del(g)/del(x_dot)} = 0
Q. Find extremal of the functional
J(x) = (0 to pi/2) ∫[x_dot^2-x^2]dt
Boundary conditions : x(0) = 0, x(pi/2) = 1
Ans :
x = sin(t) => J(x) = 0
g(t,x,x_dot) = x_dot^2-x^2 => Euler equation => x_dotdot + x = 0

## Slide 12: Minimization of a functional : J(x) = (t0 to tf) ∫ g(t,x,x_dot)dt
Euler equation
  del(g)/del(x) - d/dt{del(g)/del(x_dot)} = 0
Based on the problem formulation required boundary conditions will appear
  Either from problem formulation
  Or Obtained from solution approach
  [del(g)/del(x_dot)]T 𝛿xf + [g – [del(g)/del(x_dot)]T x_dot]𝛿tf = 0
  Kirk page no : 123 - 143

## Slide 13: Optimal control theory
Constraints
  State dynamics: x_dot = f(t,x,u). (differential equations/difference equations)
  g(x,x_dot) = x_dot - f(t,x,u) = 0
  it will always be there
  May be there or may not be present
    Constraints on the states: V(x) <= 0
    Constraints on the control: W(u) <= 0
    Constraints on state and control together : Y(x,u) <= 0
Cost function / Performance index
  J = ϕ(tf , xf) + (t0 to tf) ∫ g(t,x,u)dt
Euler-Lagrange equations (EL equations)
  By an approach similar to the static optimization
  Some concepts of variational calculus

## Slide 14: Optimal control
J = ϕ(tf, xf) + (t0 to tf) ∫ g(t,x,u)dt
ϕ(tf, xf) = (t0 to tf) ∫ [d(ϕ(t,x))/dt]dt + ϕ(t0, x0)
J = (t0 to tf) ∫{[d(ϕ(t,x))/dt]+g(t,x,u)}dt
Ja = (t0 to tf) ∫{[d(ϕ(t,x))/dt]+g(t,x,u)+ ƛT [x_dot - f(t,x,u)]}dt
= (t0 to tf) ∫ga(x(t),x_dot(t),u(t), ƛ(t),t)dt
𝛿 Ja = 0
Kirk Chapter-5 page no : 184 to 188

## Slide 15: Necessary conditions of optimality
System dynamics : x_dot = f(t,x,u)
Cost function : J = ϕ(tf , xf) + (t0 to tf) ∫ g(t,x,u)dt
Steps to solve optimal control problem
Construct a function H (called Hamiltonian function)
H = g(t,x,u) + ƛT f(t,x,u)
Necessary conditions of optimality along the optimal trajectory
  x_dot = del(H)/del(ƛ). (state equation) => differential equation
  ƛ_dot = -del(H)/del(x) (co-state equation) => differential equation
  del(H)/del(u) = 0 (optimal control equation) => algebraic equation
  Boundary conditions (required to solve the diff. eqns)
    Initial boundary conditions for state (x) is known
    However, Initial conditions for co-state (ƛ) is unknown, in general final ƛ (i.e. ƛf ) is known

## Slide 16: Numerical solution of differential eqns.
RK-4 : all the initial states x0 should be known , x_dot = f(t,x)
x_dot = f(t,x, ƛ) , x0 : known
ƛ_dot = g(t,x, ƛ), ƛ0 : unknown, ƛf : known
It is not an IVP, hence we cannot solve using RK-4 method
This kind or differential equation problem is called BVP (boundary value problem), where initial value of some variables are known, and final value of other variables are known.
  Gradient method
  Shooting method
  ……
  All these methods are iterative in nature.
    very slow to converge
    very sensitive to initial guess

## Slide 17: Gradient method
Necessary conditions of optimality:
  x_dot = del(H)/del(ƛ) =f(t,x,u). (state equation) => differential equation
  ƛ_dot = -del(H)/del(x)=h(t,x,u,ƛ) (co-state equation) => differential equation
  del(H)/del(u) = 0 (optimal control equation) => algebraic equation
Assumptions :
  control solution (u) is known => u(t) is known for all [t0, tf]
  Forward integration of state differential equation (because x0 is known)
  Backward integration of costate differential equation (because ƛf is known)
    State x is obtained from the the integrated trajectory of x.
  Control eqn. is not satisfied
  ui+1 = ui - 𝜏 [del(H)/del(u)]
  𝜏 is designer's choice, and it is generally between 0 to 1.

## Slide 18
J = q/2(Mf – 0.8)2+ (0 to tf) ∫ 1 dt
g(t,x,u) + ƛT f(t,x,u)
H = g + ƛ1 f1 + ƛ2 f2
H = g + ƛ1 f1
ƛ1_dot = -del(H)/del(M) =
ƛ1f = del(phi)/del(Mf) = q(Mf – 0.8)